## Slide 1
S-ALE Recent Development
Hao Chen, LSTC
2018 LS-DYNA USER CONFERENCE

## Slide 2: Mesh Trimming
Reduce number of S-ALE elements to save running time and memory. The following example, by trimming off elements at a distance away from the shell structures (buried inside S-ALE mesh, not shown), had a saving of 3614/9261 elements = ~40%.
http://ftp.lstc.com/anonymous/outgoing/hao/sale/models/meshtrim/saletrim.tar

## Slide 3: Mesh Trimming
*ALE_STRUCTURED_MESH |  |  |  |  | 
MSHID | PID | NBID | EBID |  | 
1 | 1 | 200001 | 200001 |  | 
CPIDX | CPIDY | CPIDZ | NID0 | LCSID | 
1001 | 1001 | 1001 | 1 | 234 | 
*ALE_STRUCTURED_MESH_TRIM |  |  |  |  | 
MSHID | COMMAND | OPER | FLIP | NID | RADIUS
1 | SPHERE | 0 | 0 | 5 | 0.1
1 | SPHERE | 1 | 0 | 5 | 0.03
Supports 4 basic geometries PLANE, CYLINDER, BOX, SPHERE; and PARTSET, SEGSET options.
Trim or keep (OPER); Inside or outside (FLIP).
Can have multiple entries; each one processed by the order of input.

## Slide 4: Mesh Trimming
Originally a box shaped mesh, trimmed by “PARTSET” option at an distance to the “LSTC” LAG structure mesh.
http://ftp.lstc.com/anonymous/outgoing/hao/sale/models/meshtrim/lstc.tar

## Slide 5: Mesh motion: FOLLOW_GC
http://ftp.lstc.com/anonymous/outgoing/hao/sale/models/meshmotion/birdstrike/bird_sale.tar

## Slide 6: Mesh Motion
*ALE_STRUCTURED_MESH |  |  |  | 
MSHID | PID | NBID | EBID | 
1 | 910002 | 1000001 | 1000001 | 
CPIDX | CPIDY | CPIDZ | NID0 | LCSID
1001 | 1002 | 1004 | 1000000 | 
*ALE_STRUCTURED_MESH_MOTION |  |  |  | 
MSHID | COMMAND | AMMGSET | EXPLIM | 
1 | FOLLOW_GC | 1 | 2.0 | 
There is only one option for now. FOLLOW_GC is to make the mesh move with the gravity center of certain AMMG groups; and expand/contract with those fluids.

## Slide 7: Example: Bird strike
AWG ERIF Test Case 5: Bird Strike on Rigid Plate http://awg.lstc.com/
Rigid plate 30”x30”; Ellipsoid bird, polar radius 10” , equatorial radii 5” with initial velocity 4200 in/s; ALE mesh 53x40x40 from (-21.75,-15.54,28.91) to (-8.5,-5.54,38.91)

## Slide 8: S-ALE Model Setup
*ALE_STRUCTURED_MESH_CONTROL_POINTS |  |  | 
1001 |  |  | 
1 |  | -21.75 | 
41 |  | -8.5 | 
*ALE_STRUCTURED_MESH_CONTROL_POINTS |  |  | 
1003 |  |  | 
1 |  | 28.9135 | 
41 |  | 38.9135 | 
*ALE_STRUCTURED_MESH_CONTROL_POINTS |  |  | 
1002 |  |  | 
1 |  | -15.5366 | 
41 |  | -5.5366 | 
FOLLOW_GC: Follow mass center of fluid(s) and expand/contract
AMMGSET: AMMG SETID of ALE fluids to follow
EXPLIM: Expansion limit =2.0 means expand at most 2 times.
*ALE_STRUCTURED_MESH |  |  |  | 
MSHID | PID | NBID | EBID | 
1 | 910000 | 100001 | 100001 | 
CPIDX | CPIDY | CPIDZ | NID0 | LCSID
1001 | 1002 | 1003 | 100000 | 
*ALE_STRUCTURED_MESH_MOTION |  |  |  | 
MSHID | COMMAND | AMMGSET | EXPLIM | 
1 | FOLLOW_GC | 1 | 2.0 | 

## Slide 9: S-ALE Trimmed Model Setup
*ALE_STRUCTURED_MESH |  |  |  |  | 
MSHID | PID | NBID | EBID |  | 
1 | 910000 | 100001 | 1000001 |  | 
CPIDX | CPIDY | CPIDZ | NID0 | LCSID | 
1001 | 1002 | 1003 | 100000 |  | 
*ALE_STRUCTURED_MESH_MOTION |  |  |  |  | 
MSHID | COMMAND | AMMGSET | EXPLIM |  | 
1 | FOLLOW_GC | 1 | 2.0 |  | 
*ALE_STRUCTURED_MESH_TRIM |  |  |  |  | 
MSHID | COMMAND | OPER | FLIP | PSETID | OFFSET
1 | PARTSET |  | 1 | 910001 | 2.25
PARTSET: TRIM by reference geometry prescribed by LAG shell part set
OPER: To TRIM (0) or KEEP (1)
FLIP: To trim OUTSIDE (0) or INSIDE (1)
PSETID: PARTSET ID
OFFSET: S-ALE elements farther than 2.25 are deleted.

## Slide 10: Results

## Slide 11: Comparison: ALE, S-ALE, S-ALE trim
METHODS | # of Elements | SMP 1 Core | SMP Savings | MPP 4 Core | MPP Savings
ALE | 84800 | 1204 s |  | 321 s | 
S-ALE | 84800 | 675 s | 44% | 191 s | 40%
S-ALE trim | 43219 | 426 s | 65% | 112 s | 65%

## Slide 12: Multiple Meshes
Contact between bags DISABLED
Contact between bags ENABLED
Two pressurized airbags, each inside an independent S-ALE mesh.
S-ALE supports multiple meshes. By default, these meshes are independent from each other, i.e. they don’t know the existence of other meshes. These meshes can occupy different spatial domains or the SAME domain.

## Slide 13: Multiple Meshes Merged
Seven meshes merge into one part.

## Slide 14: Motivation
Soil & HE needs a much smaller mesh box than air. The above two meshes setup reduced mesh usage from 6 million to 4 million.

## Slide 15: Mesh Merging
Multiple *ALE_STRUCTURED_MESH cards. Different MSHID. SAME PID.
Well prepared for the future MPP load rebalancing.
*ALE_STRUCTURED_MESH |  |  |  |  | 
MSHID | PID | NBID | EBID |  | 
CPIDX | CPIDY | CPIDZ | NID0 | LCSID | 
*ALE_STRUCTURED_MESH |  |  |  |  | 
MSHID | PID | NBID | EBID |  | 
CPIDX | CPIDY | CPIDZ | NID0 | LCSID | 
SAME PID

## Slide 16
Thank You